## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: Multiplication and Division
Multiplication and Division Instructions
MUL – unsigned multiply
IMUL – signed multiply
DIV – unsigned division
IDIV – signed división

## Slide 3: MUL Instruction (Unsigned Multiply) iiVa
The MUL (unsigned multiply) instruction multiplies an 8-, 16-, 32- or 64- bit operand by either AL, AX, EAX, or RAX.
The one-operand instruction formats are:
    MUL reg/mem8 ;16-bit product
    MUL reg/mem16 ;32-bit product
    MUL reg/mem32 ;64-bit product
Implicit multiplicand: AL, AX or EAX.
Check CARRY flag after MUL for significant bits in the upper half of the product.
The product is twice the size of the multiplicand or the multiplier.
Multiplicand | Multiplier | Product
AL | reg/mem8 | AH:AL = AL * reg/mem8
AX | reg/mem16 | DX:AX = AX * reg/mem16
EAX | reg/mem32 | EDX:EAX = EAX * reg/mem32

## Slide 4: MUL Examples 1
2000h * 100h, using 16-bit operands:
.DATA
val1 WORD 2000h
val2 WORD 100h
.CODE
MOV AX,val1
MUL val2 ; DX:AX = 00200000h, CF=1
The CARRY flag indicates whether or not the upper half of the product contains significant digits.
MOV EAX,12345h
MOV EBX,1000h
MUL EBX ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 5: MUL Examples 2
5h * 10h, using 8-bit operands:
.CODE
MOV AL,05h
MOV BL,10h
MUL BL ; AH:AL = 0050h, CF=0

## Slide 6: Your turn . . . 1
MOV AX,1234h
MOV BX,100h
MUL BX
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?

## Slide 7: Your turn . . . 2
MOV EAX,00128765h
MOV ECX,10000h
MUL ECX
What will be the hexadecimal values of EDX, EAX, and the Carry flag after the following instructions execute?

## Slide 8: IMUL Instruction (Signed Multiply)
IMUL (signed integer multiply ) multiplies an 8-, 16-, 32- or 64- bit operand by either AL, AX, EAX, or RAX.
Preserves the sign of the product by sign-extending it into the upper half of the destination register
The one-operand instruction formats are:
    IMUL reg/mem8 IMUL reg/mem32
    IMUL reg/mem16 IMUL reg/mem64
CF and OF are set if the upper half of the product is not a sign extension of the lower half.
Multiplicand | Multiplier | Product
AL | reg/mem8 | AH:AL = AL * reg/mem8
AX | reg/mem16 | DX:AX = AX * reg/mem16
EAX | reg/mem32 | EDX:EAX = EAX * reg/mem32

## Slide 9: IMUL Examples
Example: multiply 48 * 4, using 8-bit operands:
MOV AL,48 ; AL = 48 = 30h
MOV BL,4
IMUL BL ; AX(AH:AL) = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL.
Example: multiply 48 * 4, using 16-bit operands:
MOV AX,48
MOV BX,4
IMUL BX ; DX:AX = 000000C0h, OF=0
OF=0 because DX is a sign extension of AX.

## Slide 10: IMUL Instruction (Signed Multiply)
Two-operand 16-bit formats, 16-bit product:
    IMUL reg16,reg/mem16
    IMUL reg16,imm8
    IMUL reg16,imm16
Two-operand 32-bit formats, 32-bit product:
    IMUL reg32,reg/mem32
    IMUL reg32,imm8
    IMUL reg32,imm32
Two-operand 64-bit formats.
Multiplicand | Multiplier | Product
reg16 | reg/mem16 | reg16 = reg16 * reg/mem16
reg16 | imm8/imm16 | reg16 = reg16 * imm8/imm16
reg32 | reg/mem32 | reg32 = reg32 * reg/mem32
reg32 | imm8/imm32 | reg32 = reg32 * imm8/imm32
Two-operand IMUL formats truncate the product. When significant digits are lost OF and CF are set.

## Slide 11: IMUL Instruction (Signed Multiply)
Three-operand 16-bit formats:
    IMUL reg16,reg/mem16,imm8
    IMUL reg16,reg/mem16,imm16
Three-operand 32-bit formats:
    IMUL reg32,reg/mem32,imm8
    IMUL reg32,reg/mem32,imm32
Three-operand 64-bit formats.
Multiplicand | Multiplier | Product
reg16 | reg/mem16 | reg16 = reg/mem16 * imm8
reg16 | imm8/imm16 | reg16 = reg/mem16 * imm16
reg32 | reg/mem32 | reg32 = reg/mem32 * imm8
reg32 | imm8/imm32 | reg32 = reg/mem32 * imm32
Three-operand IMUL formats truncate the product. When significant digits are lost OF and CF are set.

## Slide 12: IMUL Examples
Example: multiply 4,823,424 * -423:
MOV EAX,4823424
MOV EBX,-423
IMUL EBX ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF=0, CF=0 because EDX is a sign extension of EAX.

## Slide 13: Your turn . . . 3
MOV AX,8760h
MOV BX,100h
IMUL BX
What will be the hexadecimal values of DX, AX, and the OVERFLOW flag after the following instructions execute?

## Slide 14: DIV Instruction (Unsigned Divide)
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, 32-bit and 64-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
    DIV reg/mem8 ;16-bit dividend
    DIV reg/mem16 ;32-bit dividend
    DIV reg/mem32 ;64-bit dividend
    DIV reg/mem64
Dividend | Divisor | Quotient | Reminder
AH:AL | reg/mem8 | AL | AH
DX:AX | reg/mem16 | AX | DX
EDX:EAX | reg/mem32 | EAX | EDX

## Slide 15: DIV Examples
Divide 8003h by 100h, using 16-bit operands, 32-bit dividend
MOV DX,0 ; clear dividend, high
MOV AX,8003h ; dividend, low
MOV CX,100h ; divisor
DIV CX ; AX = 0080h, DX = 3
Same division, using 32-bit operands, 64-bit dividend:
MOV EDX,0 ; clear dividend, high
MOV EAX,8003h ; dividend, low
MOV ECX,100h ; divisor
DIV ECX ; EAX = 00000080h, EDX = 3

## Slide 16: DIV conditions
All arithmetic status flag values are undefined (?) after executing DIV instructions.
What happens if the Quotient doesn’t fit the destination operand (register)?
  A divide overflow condition results, causing a CPU interrupt and the current program halts.
What happens if the divisor is zero?
  A division by zero condition results, causing a CPU interrupt and the current program halts.
  To prevent division by zero, test de divisor before dividing.

## Slide 17: Your turn . . . 4
MOV DX,0087h
MOV AX,6000h
MOV BX,100h
DIV BX
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:

## Slide 18: Your turn . . . 5
MOV DX,0087h
MOV AX,6002h
MOV BX,10h
DIV BX
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:

## Slide 19: Signed Integer Division (IDIV)
Signed integers must be sign-extended before division takes place
  fill high byte/word/doubleword with a copy of the low byte/word/doubleword's sign bit
For example, the high byte contains a copy of the sign bit from the low byte:

## Slide 20: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide important sign-extension operations:
  CBW (convert byte to word) extends AL into AH
  CWD (convert word to dword) extends AX into DX
  CDQ (convert dword to qword) extends EAX into EDX
  CQO (convert qword to oword) extends RAX into RDX
Example:
    .DATA
    dwordVal SDWORD -101 ; FFFFFF9Bh
    .CODE
    MOV EAX,dwordVal
    CDQ ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 21: IDIV Instruction
IDIV (signed divide) performs signed integer division
Same syntax and operands as DIV instruction
Example: 8-bit division of –48 by 5
MOV AL,-48 ; AL = D0h (-30h)
CBW ; extend AL into AH=FFh
MOV BL,5
IDIV BL ; AL = -9, AH = -3

## Slide 22: IDIV Examples
Example: 32-bit division of –48 by 5
MOV EAX,-48 ; EAX = FFFFFFD0h
CDQ ; extend EAX into EDX
MOV EBX,5
IDIV EBX ; EAX = -9, EDX = -3
Example: 16-bit division of –48 by 5
MOV AX,-48 ; AX = FFD0h
CWD ; extend AX into DX
MOV BX,5
IDIV BX ; AX = -9, DX = -3

## Slide 23: Your turn . . . 6
MOV AX,0FDFFh ;AX= -513 = -0201h
CWD
MOV BX,100h ;BX= 256
IDIV BX
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:

## Slide 24: IDIV conditions
All arithmetic status flag values are undefined (?) after executing IDIV instructions.
What happens if the Quotient doesn’t fit the destination operand (register)?
  A divide overflow condition results, causing a CPU interrupt and the current program halts.
What happens if the divisor is zero?
  A division by zero condition results, causing a CPU interrupt and the current program halts.
  To prevent division by zero, test de divisor before dividing.

## Slide 25: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos, bxh
03-oct-2019