## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: x86 Floating-Point
Floating-Point Binary Representation
Floating-Point Unit

## Slide 3: Floating-Point Unit
FPU Data Register Stack, core of the FPU
Eight individually addressable 80-bit FPU Data Registers named R0 through R7
Three-bit field named TOP in the FPU status word identifies then FPU Data Register Number that is currently the top of stack.

## Slide 4: FPU Stack: Push and Pop
PUSH / LOAD operation
  LOAD operand
    TOP - -
    ST(0) <- operand
POP / STORE operation
  STORE operand
    operand <- ST(0)
    TOP + +

## Slide 5: X86 Floating-Point Unit
FPU Stack, initial value, TOP = 1002 , ST(0) is R4
FPU Stack after pushing 1.0 and 2.0
TOP--, ST(0) <- 1.0; TOP--, ST(0) <- 2.0
TOP = ___? TOP = ___?

## Slide 6: Issues
FPU stack works in a circular fashion
Situations
  If TOP equals 7 (R7) before the POP, TOP++ reaches R0.
  PUSHing a value into a full stack, can overwrite a data register, launching an exception.

## Slide 7: FPU Special-Purpose Registers
• Opcode register: stores opcode of last non-control instruction executed
• Control register: controls precision and rounding method for calculations
• Status register: top-of-stack pointer, condition codes, exception warnings
• Tag register: indicates content type of each register in the register stack (size)
• Last instruction pointer register: pointer to last non-control executed instruction
• Last data (operand) pointer register: points to data operand used by last executed instruction

## Slide 8: FPU Stack
Stack does it great evaluating expressions in postfix format
Infix expression
  (5*6)+4
Postfix expression
  5 6 * 4 +

## Slide 9: Floating-Point Exceptions
Five types of exception conditions
  Invalid operation
  Divide by zero
  Denormalized operand
  Numeric overflow
  Inexact precision
Each has a corresponding mask bit
  if set when an exception occurs, the exception is handled automatically by FPU
  if clear when an exception occurs, a software exception handler is invoked

## Slide 10: FPU Instruction Set - 1
Instruction mnemonics begin with letter F
Second letter identifies data type of memory operand
  B = BCD
  I = binary integer
  no letter: floating point, real numbers
Examples
  FB BL D load Binary Coded Decimal
  F I S T P store integer and pop stack
  F M U L multiply floating-point operands

## Slide 11: FPU Instruction Set - 2
Operands
  zero, one, or two
  no immediate operands
  no general-purpose registers (EAX, EBX, ...)
  integers must be loaded (pushed) from memory onto the stack and converted to floating-point before being used in calculations
  if a FPU instruction has two operands, one must be a FPU register

## Slide 12: FP Data Types
.DATA
One REAL4 21.3
Two REAL8 781.65
Four REAL8 2.03E-7

## Slide 13: Floating-Point I/O
Irvine32 library procedures
  ReadFloat
    reads FP value from keyboard, pushes it on the FPU stack
  WriteFloat
    writes value from ST(0) to the console window in exponential format
  ShowFPUStack
    displays contents of FPU stack

## Slide 14: Floating-Point Instruction Set
Basic categories of instructions.
Data transfer
Basic arithmetic
Comparison
Transcendental
Load constants (specialized predefined constants only)
And, many more . . .

## Slide 15: First FPU Instruction
FINIT
  The FINIT instruction initializes the FPU.
  Sets the initial states of the FPU.
  Control instruction

## Slide 16: Data Transfer Instructions
Very First Ones
  FLD
  FST
  FSTP

## Slide 17: Load a Floating-Point Value
FLD
LoaDs Floating point operand from memory into the top of the FPU stack, ST(0)
TOP--; ST(0) <- memory location, a push.

## Slide 18: FLD
FLD Example

## Slide 19: Memory Operand Types
Addressing operand types are similar to the integer operand

## Slide 20: Store Floating-Point Value
FST
  copies floating point operand from the top of the FPU stack and store it into memory
  memory location <- ST(0)
FSTP
  pops the stack after copying
  memory location <- ST(0), TOP++, a pop

## Slide 21: Arithmetic Instructions
Same operand types as FLD and FST

## Slide 22: Floating-Point Add
FADD
  adds source to destination
  No-operand version, pops the FPU stack

## Slide 23: Floating-Point Add
FADD Examples:

## Slide 24: Floating-Point Subtract
FSUB
  subtracts source from destination.
  No-operand version, pops the FPU stack after subtracting

## Slide 25: Floating-Point Subtract
Example:

## Slide 26: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
26-nov-2019