## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: HLL Structured instructions. via
Algorithm ---- program
Structured thinking
Algorithm structures
    Selectives: If-then, if-then-else, switch-case
    Repetitives: while, for, do-while, repeat
There are not such instructions in machine language.
The programmer must do the implementation.

## Slide 3: Flags Affected by Arithmetic
The CPU has a number of Status Flags that reflect the outcome of arithmetic and bitwise operations (machine instruction)
  based on the contents of the destination operand
  Instructions ADD, CLC, CMP, DEC, INC, IMUL, NEG, TEST, and many more . . . except MOV (*)
Essential flags:
  ZeroF, SignF, CarryF, OverflowF, AxiliaryF, ParityF
(*)Th e MOV instruction never affects the flags.

## Slide 4: Status Flags - Review iVc
The Zero flag ZF is set when the destination (result) equals zero.
The Carry flag CF is set when a result that is too large (or too small) for the destination; unsigned out-of-range result value.
The Sign flag SF is set if the destination is negative, otherwise it is clear. A Signed result value.
The Overflow flag OF is set when a destination is a signed out-of-range result value.
The Auxiliary Carry flag AF is set when an operation produces a carry out from bit 3 to bit 4.
The Parity flag PF is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
CONDITIONAL JUMPS WILL USE THESE FLAGS

## Slide 5: CPU flags affected
Assembly Language for x86 Processors Book
  Appendix B. The x86 Instruction Set

## Slide 6: 16-bit FLAGS register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | nt | iop | iop | OF | df | if | tf | SF | ZF | 0 | AF | 0 | PF | 1 | CF
FLAGS categories
STATUS flags: OF, SF, ZF, AF, PF, CF
CONTROL flags: tf, if, df
SYSTEM flags: iop, nt
Reserved bits: 0s and 1.

## Slide 7: 32-bit EFLAGS register
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | nt | iop | iop | OF | df | if | tf | SF | ZF | 0 | AF | 0 | PF | 1 | CF
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | id | vip | vif | ac | vm | rf
FLAGS categories
STATUS flags: OF, SF, ZF, AF, PF, CF
CONTROL flags: tf, if, df
SYSTEM flags: iop, nt, rf, vm, ac, vif, vip, id
Reserved bits: 0s and 1.

## Slide 8: 64-bit RFLAGS register
63 | 62 | 61 | 60 | 59 | 58 | 57 | 56 | 54 | 54 | 53 | 52 | 51 | 50 | 49 | 48
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
0 | nt | iop | iop | OF | df | if | tf | SF | ZF | 0 | AF | 0 | PF | 1 | CF
31 | 30 | 29 | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20 | 19 | 18 | 17 | 16
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | id | vip | vif | ac | vm | rf
47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 9: Concept Map
status flags
ALU
conditional jumps
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
CPU
executes
executes

## Slide 10: Signed and Unsigned Integers
A CPU Hardware Viewpoint
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
YOU, the PROGRAMMER, are solely responsible for using the correct data type with each instruction

## Slide 11: ZERO Flag (ZF)
MOV CX,1 ; none flag is changed
SUB CX,1 ; CX = 0, ZF = 1 , CF = __
MOV AX,0FFFFh
INC AX ; AX = 0, ZF = 1 , CF = __
INC AX ; AX = 1, ZF = 0 , CF = __
The ZERO flag is set when the result of an operation produces zero in the destination operand.
Remember...
A flag is set when it equals 1.
A flag is clear when it equals 0.

## Slide 12: CARRY Flag (CF)
The CARRY flag is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
MOV AL,0FFh
ADD AL,1 ; CF = 1, AL = 00 , ZF = __
; Try to go below zero:
MOV AL,0
SUB AL,1 ; CF = 1, AL = FF , ZF = __

## Slide 13: Auxiliary Carry Flag. vIaiiVb
The Auxiliary Carry (AC) Flag indicates a carry or a borrow out of bit 3 to bit 4 in the destination operand.
Example:
MOV AL,0Fh MOV AL,22h
ADD AL, 1 ; ACF=1 SUB AL, 8h ;ACF=1
The develope
0 0 0 0 1 1 1 1 0 0 1 0 0 0 1 0
+ 0 0 0 0 0 0 0 1 - 0 0 0 0 1 0 0 0
0 0 0 1 0 0 0 0 0 0 0 1 1 0 1 0
Related operations: BCD (Binary-Coded Decimal) arithmetic operations in four bits. The digits 0..9 are represented en four bits.

## Slide 14: SIGN Flag (SF)
MOV CX,0
SUB CX,1 ; CX = -1, SF = 1
ADD CX,2 ; CX = 1, SF = 0
The SIGN flag is set when the destination signed operand is negative. The flag is clear when the destination is positive.
The SIGN flag is a copy of the destination's highest bit:
MOV AL,0
SUB AL,1 ; AL = 11111111b, SF = 1
ADD AL,2 ; AL = 00000001b, SF = 0

## Slide 15: Your turn . . .
MOV AX,00FFh
ADD AX,1 ; AX= SF= ZF= CF=
SUB AX,1 ; AX= SF= ZF= CF=
ADD AL,1 ; AL= SF= ZF= CF=
MOV BH,6Ch
ADD BH,95h ; BH= SF= ZF= CF=
MOV AL,2
SUB AL,3 ; AL= SF= ZF= CF=
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:

## Slide 16: OVERFLOW Flag (OF)
The OVERFLOW flag is set when the signed result of an operation is invalid or out of range.
; Example 1
MOV AL,+127
ADD AL,1 ; OF = __, AL = __
; Example 2
MOV AL,7Fh ; OF = __, AL = __
ADD AL,1

## Slide 17: A Rule of Thumb / unsigned
When ADDing two integers, remember that the Overflow flag is only set when . . .
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF =
mov al,-2
add al,+127 ; OF =
mov al,+2
add al,+127 ; OF =
__
__
__

## Slide 18: NEG Instruction.
.DATA
valB BYTE 1,0
valC SBYTE -128
.CODE
NEG valB ; CF = _, OF = _
NEG [valB + 1] ; CF = _, OF = _
NEG valC ; CF = _, OF = _
The processor implements NEG using the following internal operation:
operand = 0 – operand ; or
operand = 0 + (-operand) ; adding viewpoint

## Slide 19: Your turn . . .
MOV AL,-128
NEG AL ; CF = OF =
MOV AX,8000h
ADD AX,2 ; CF = OF =
MOV AX,0
SUB AX,2 ; CF = OF =
MOV AL,-5
SUB AL,+125 ; CF = OF =
What will be the values of the given flags after each operation?

## Slide 20: Parity Flag. vIaiiVb
The Parity Flag (PF) is set when the least significant byte of the destination operand has an even number of 1 bits.
Example:
MOV AL, 10001100b
ADD AL, 00000010b ; AL = 10001110, PF = 1
SUB AL, 10000000b ; AL = 00001110, PF = 0

## Slide 21: Keeping track of Flags
Related instructions
LAHF – Load status flags into AH
    AH  Low byte of EFLAGS (S, Z, 0, A, 0, P, 1, C)
SAHF – Store AH into status flags
    Low byte of EFLAGS (S, Z, 0, A, 0, P, 1, C)  AH
.DATA
one BYTE ?
.CODE
LAHF
MOV one, AH
; following CODE
MOV BL, one
- - -
MOV AH, one
SAHF

## Slide 22: Instructions around the Carry flag
Set carry flag
    STC ;CF=1
Clear carry flag
    CLC ;CF=0
Complement carry flag
    CMC ;CF= 1s complement of CF
Add carry flag
    ADC opd1,opd2 ; opd1  opd1 + opd2 + CF

## Slide 23: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos
12-sep-2019