## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: Jconds
Hard to use them, because the predecessor instructions usually affect several flags at the same time, not necessaraly one flag.

## Slide 3: CMP in Structured Instructions
CMP instruction is used to create conditional logic structures
When follow CMP with a conditional jump instruction, the result is the assembly language equivalent of an IF or a WHILE statement, or any other structured High Level Language instruction.

## Slide 4: CMP Instruction
Syntax: CMP leftOp, rightOp
Compares the leftOp operand to the rightOp operand
  Nondestructive implied subtraction of rightOp from leftOp (neither operand is changed)
Logic: leftOp - rightOp
The comparation affect all the flags.
The following operand combinations are permitted
  CMP reg, reg
  CMP reg, mem
  CMP reg, imm
  CMP mem, reg
  CMP mem, imm

## Slide 5: CMP of two Unsigned operands
Example 1: it works when leftOp == rightOp
MOV AL,5
CMP AL,5 ; ZF=1, CF=0
Example 2: it works when leftOp < rightOp
MOV AL,4
CMP AL,5 ; ZF=0, CF=1
Example 3: it works when leftOp > rightOp
MOV AL,6
CMP AL,5 ; ZF = 0, CF = 0

## Slide 6: CMP + Jconds usage
Example 1 looks like an IF
Example2 looks like repetive
cmp EAX,uno
Jcond la1
. . .
. . .
la1:. . .
la2:
. . .
. . .
cmp dos,EBX
Jcond la2
. . .

## Slide 7: Jconds Based on Equality
For UNSIGNED or SIGNED use.

## Slide 8: Jconds Based on Unsigned operands
Better use JA, JAE, JB and JBE Above, Below

## Slide 9: Examples, Unsigned- 1
CMP EAX,EBX
JA Larger
Task: Jump to a label if unsigned EAX is greater than EBX
Solution: Use CMP, followed by JA
CMP EAX,Val1
JBE L1 ; below or equal
Jump to label L1 if unsigned EAX is less than or equal to Val1

## Slide 10: CMP of two Signed operands
Example 4: it works when leftOp > rightOp
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
Example 5: it works when leftOp < rightOp
mov al,-1
cmp al,5 ; Sign flag != Overflow flag
Example 6: it works when leftOp == rightOp
mov al,-1
cmp al,-1 ; ZF=1, CF=don´t care

## Slide 11: Jconds Based on Signed operands
Better use JG, JGE, JL and JLE Greater, Lower

## Slide 12: Examples, Signed- 2
CMP EAX,EBX
JG Greater
Task: Jump to a label if signed EAX is greater than EBX
Solution: Use CMP, followed by JG
CMP EAX,Val1
JLE L1
Jump to label L1 if signed EAX is less than or equal to Val1

## Slide 13: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
08-oct-2018