## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: IF-then, IF-then-else, While, DO-while in Assembly

## Slide 3: IF-then implementation
  High Level L Assembly
  IF(LfOp cmpOpr RhOp) CMP LfOp, RhOp
  { JnoCMP outIF
  block. .; block. .
} outIF: ;next instruc
The IF Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP)

## Slide 4: IF-then examples
  High Level L Assembly
  Large = BX; MOV Large,BX
  IF(AX > BX) CMP AX,BX
  { JBE outIF ;Jump if AX<=BX
  Large = AX; MOV Large,AX
} outIF:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
  High Level L Assembly
  Small = AX; MOV Small,AX
  IF(BX < AX) CMP BX,AX
  { JGE outIF ;Jump if BX>=AX
  Small = BX; MOV Small,BX
} outIF:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small

## Slide 5: IF-then-else implementation
  High Level L Assembly
  IF(LfOp cmpOp RhOp) CMP LfOp,RhOp
  { JnoCMP inELSE
  block1. .; block1. .
} JMP outIF
else inELSE:
{
black2. .; block2. .
} outIF: ;next instruc
The IF Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP). A JMP is needed at the end of block1 to avoid enter into the ELSE area.

## Slide 6: WHILE implementation
  High Level L Assembly
  WHILE(LfOp cmpOp RhOp) inWHILE: CMP LfOp,RhOp
  { JnoCMP outWHILE
  block. .; block. .
} JMP inWhile
outWHILE: ;nextinstruc
The WHILE Assembly implementation involves a conditional jump for the negative of the comparison (JnoCMP). After the block it requieres to jump back to do compare.

## Slide 7: WHILE example
  High Level L Assembly
  EAX=45; MOV EAX,45
  EBX=1; MOV EBX,1
  WHILE(EBX < 6) inWHILE: CMP EBX,6
  { JGE outWHILE
  EAX=EAX-2; SUB EAX,2
  EBX=EBX+1; INC EBX
} JMP inWhile
outWHILE: ;nextinstruc
The WHILE Assembly implementation involves a conditional jump for the same comparison (JnoCMP). After the block it requires to jump back to do compare. Example signed.

## Slide 8: DO-WHILE implementation
  High Level L Assembly
  DO inDO:
  block. .; block. .
  WHILE(LfOp cmpOp RhOp) CMP LfOp,RhOp
  JsaCMP inDO
;nextinstruc
The DO-WHILE Assembly implementation involves a conditional jump for the same comparison (JsaCMP). After the block it requires to jump back to do compare.

## Slide 9: DO-WHILE example
  High Level L Assembly
  EAX=50; MOV EAX,50
  EBX=0; MOV EBX,0
  DO inDO:
  EAX=EAX+1; INC EAX
  EBX=EBX+1; INC EBX
  WHILE(EBX < 4) CMP EBX,4
  JL inDO
;nextinstruc
The DO-WHILE Assembly implementation involves a conditional jump for the positive of the comparison (JsaCMP). After the block it requires to jump back to do compare. Example signed.

## Slide 10: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
08-oct-2019