## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: Bitwise Boolean Instructions
To build up compound conditional expressions for IF-then, IF-then-else, WHILE, DO-WHILE, REPEAT-UNTIL and FOR, logical Boolean instructions are required.
  (A > B) && (C <= 5)
  && is the Logical Boolean operator and, in a HLL
Issue: there are not logical Boolean Assembly instructions,
Only Bitwise (bit to bit): AND, OR, XOR, NOT, TEST

## Slide 3: AND Instruction
AND, bitwise, bit to bit
Syntax: AND destination, source
The following operand combinations are permitted
  AND reg, reg
  AND reg, mem
  AND reg, imm
  AND mem, reg
  AND mem, imm
Operands can be 8, 16, 32, or 64 bits, must be same size
Bit masking with the source operand.
Set INTERSECTION of bits

## Slide 4: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands
Flags
  Clears Overflow, Carry
  Modifies Sign, Zero, and Parity
Syntax:
    AND destination, source
  (same operand types as MOV)
AND
Bit masking, source: 0 in source clears a bit, 1 leaves it unchanged.

## Slide 5: OR Instruction
OR, bitwise, bit to bit
Syntax: OR destination, source
The following operand combinations are permitted
  OR reg, reg
  OR reg, mem
  OR reg, imm
  OR mem, reg
  OR mem, imm
Operands can be 8, 16, 32, or 64 bits, must be same size
Useful when you want to set one or more bits without affecting the other bits
Set UNION of bits

## Slide 6: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands
Flags
  Clears Overflow, Carry
  Modifies Sign, Zero, and Parity
Syntax:
    OR destination, source
OR
1 in source set a bit, 0 leaves it unchanged.

## Slide 7: XOR Instruction
Performs a Boolean eXclusive-OR bitwise operation between each pair of matching bits in two operands
XOR with 0 retains its value, with 1 reverses value
Flags
  Clears Overflow, Carry
  Modifies Sign, Zero, and Parity
Syntax:
    XOR destination, source
XOR
XOR is a useful way to toggle (invert) the bits in an operand.

## Slide 8: NOT Instruction
Performs a Boolean NOT bitwise operation on a single destination operand
The following operand combinations are permitted
  NOT reg
  NOT mem
Flags
  No flags are affected
Syntax:
    NOT destination
NOT
Results called one’s complement
Set COMPLEMENT of bits

## Slide 9: Bit-Mapped Set Operations
Set Complement
    MOV EAX, SetX
    NOT EAX
Set Intersection
    MOV EAX, setX
    AND EAX, setI
Set Union
    MOV EAX, setX
    OR EAX,setU

## Slide 10: ASCII Code

## Slide 11: Applications (1 of 4)
mov al,'a' ; AL = 01100001b, ‘a’
and al,11011111b ; AL = 01000001b, ‘A’
Task: Convert the character in AL to UPPER CASE.
Solution: Use the AND instruction to clear bit 5.

## Slide 12: Applications (2 of 4)
MOV AL,6 ; AL = 00000110b, 6
OR AL,00110000b ; AL = 00110110b, ‘6’
Task: Convert a binary decimal byte into its equivalent ASCII Decimal Digit.
Solution: Use the OR instruction to set bits 4 and 5.
The ASCII digit '6' = 00110110b

## Slide 13: Applications (3 of 4)
MOV AX, wordVal
AND AX, 1 ; low bit set?
JZ EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.
Your turn: Write code that jumps to a label if an integer is negative.

## Slide 14: Applications (4 of 4)
OR AL,AL
JNZ IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 15: TEST Instruction
Performs a nondestructive AND bitwise operation between each pair of matching bits in two operands
No operands are modified.
Always clears the Overflow and Carry flags.
Modifies the Sign, Zero, and Parity flags.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
TEST AL,00000011b
JNZ ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
TEST AL,00000011b
JZ ValueNotFound
TEST AL,000Bh
JNZ ValueFound

## Slide 16: Example
The value 0000 0011 in this example is called a bit mask.
TEST AL,00000011b
0 0 1 0 0 1 0 1 <- AL input value
0 0 0 0 0 0 1 1 <- test value
0 0 0 0 0 0 0 1 <- result: ZF = 0
TEST AL,00001001b
0 0 1 0 0 1 0 0 <- AL input value
0 0 0 0 1 0 0 1 <- test value
0 0 0 0 0 0 0 0 <- result: ZF = 1
The value 0000 1001 in this example is called a bit mask.

## Slide 17: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
10-oct-2019