## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: STACK
STACK data structure
A STACK of values (data)
  values are only added to the top (PUSH operation)
  values are only removed from the top (POP operation)
  LIFO (Last-in, First-out) data structure

## Slide 3: Runtime STACK
STACK inside every Process
Managed by the CPU, using a stack pointer register
  ESP (Extended Stack Pointer)
    ESP always points to the last value added

## Slide 4: PUSH operation 1
A PUSH operation decrements the stack pointer by n (2 [16 bits] or 4 [32 bits]), and copies a value into the location pointed to by the stack pointer ESP.
    ESP  ESP – n ; n=4 with a 32-bit operand
    STACK [ESP]  reg/var/value

## Slide 5: PUSH Instruction
PUSH syntax, ESP  ESP – n and saves:
  PUSH reg/mem16 ; n=2 for 16-bit operand
  PUSH reg/mem32 ; n=4 for 32-bit operand
  PUSH reg/mem64 ; n=8 for 64-bit operand
  PUSH imm32 ; n=4 for 32-bit operand
  PUSH imm64 ; n=8 for 64-bit operand

## Slide 6: PUSH operation 2
Same stack after pushing two more integers:
The stack grows downward. The area below ESP is always available (unless the stack has overflowed).

## Slide 7: POP Operation
Copies value at STACK[ESP] into a register or variable.
  Reg/Var  STACK[ESP]
Adds n to ESP, where n is either 2 or 4.
  value of n depends on the attribute of the operand receiving the data
  ESP  ESP + n

## Slide 8: POP Instruction
POP syntax: recovers and ESP  ESP + n:
  POP r/m16 ; n=2 for 16-bit operand
  POP r/m32 ; n=4 for 32-bit operand
  POP r/m64 ; n=8 for 64-bit operand

## Slide 9: Using PUSH and POP
Save and restore registers when they contain important values. PUSH and POP instructions occur in the opposite order.
.DATA
dwordVal DWORD 675
.CODE
PUSH ESI ; push registers
PUSH ECX
PUSH EBX
MOV ESI,OFFSET dwordVal ; display some memory
MOV ECX,LENGTHOF dwordVal
MOV EBX,TYPE dwordVal
CALL DumpMem
POP EBX ; restore registers
POP ECX ; aware of LIFO
POP ESI

## Slide 10: Related Instructions
PUSHFD and POPFD
  push and pop the EFLAGS register
PUSHAD pushes the 32-bit general-purpose registers on the stack
  order: EAX, ECX, EDX, EBX, ESP, EBP, ESI, EDI
POPAD pops the same registers off the stack in reverse order
PUSHA and POPA, do the same for 16-bit registers
  order: AX, CX, DX, BX, SP, BP, SI, DI

## Slide 11: PUSHAD
The value pushed for the ESP register is its value before prior to pushing the first register.
Temporary = ESP;
Push(EAX);
Push(ECX);
Push(EDX);
Push(EBX);
Push(Temporary);
Push(EBP);
Push(ESI);
Push(EDI);

## Slide 12: POPAD
The ESP register is incremented after each register is loaded.
EDI = Pop(); ESP=ESP+4
ESI = Pop(); ESP=ESP+4
EBP = Pop(); ESP=ESP+4
ESP = ESP + 4; //skip next 4 bytes of stack
EBX = Pop(); ESP=ESP+4
EDX = Pop(); ESP=ESP+4
ECX = Pop(); ESP=ESP+4
EAX = Pop(); ESP=ESP+4

## Slide 13: Stack applications - 1
Temporary save area for registers, once the registers end a set of operations, their original values can be restored.
The stack provides temporary storage for local variables.

## Slide 14: Stack applications - 2
The Call for a procedure, saves an address that uses up the Return of the procedure called.

## Slide 15: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
17-oct-2019