## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: Intel Microprocessor Evolution
Intel 8080, 8088
Intel 8086
Intel 80286
IA-32 processor family
IA-64 processor family
Microprocessors / Computer Systems

## Slide 3: Early Intel Microprocessors
Intel 8080
  8-bit registers, 32-bit integers
  S-100 BUS architecture, 8-bit data bus
  64KB addressable RAM (____-bit addressing)
  MS-DOS Operating System
  8-inch floppy disks!
Intel 8086
  IBM-PC Used 8086
  16-bit registers
  16-bit data bus
  1 MB addressable RAM (___-bit addressing)
  separate floating-point unit (8087)
  Backward-Compatibility: this approach allows older software (binary) to run on newer computers.

## Slide 4: The IBM-PC/AT
Intel 80286
  16-bit microprocessor registers
  16 MB addressable RAM (___-bit addressing)
  24-bit address bus
  Protected memory
  several times faster than 8086
  introduced IDE (Integrated Drive Electronics) BUS architecture
  Separate 80287 floating point unit (FPU)

## Slide 5: Intel IA-32 (32-Bit x86) Family
Intel386 (80386)
  __ GB addressable RAM, 32-bit data registers, 32-bit address, paging (virtual memory)
  Windows and Linux Operating System
Intel486
  instruction pipelining
  FPU, inside the main chip
Pentium
  superscalar, 32-bit address bus, 64-bit internal data path

## Slide 6: IA-32 (32-Bit x86) Processor Architecture
Modes of operation
Basic execution environment
Floating-Point Unit FPU

## Slide 7: IA-32 Modes of Operation -1
Protected Mode
  native state for 80x86 CPUs (Windows, Linux)
  every resource can be used
  4GB of central memory, 32-bit addresses
  programs (processes) given separate memory areas
  security: every process can not address other process area

## Slide 8: IA-32 Modes of Operation -2
Real-Address Mode
  implements programming environment of Intel 8086 processor
  1 MB of central memory, 20-bit addresses
  native MS-DOS
  backward compatibility
  programs can cause MS-DOS crash
  The MS-DOS works like a virtual machine

## Slide 9: IA-32 Modes of Operation - 3
System Management Mode
  Provides OS with:
    boot configuration
    power management (power-on, battery level, shutdown)
    system security
    diagnostics
    disks defragmenter
  This functions are implemented by computer (hardware) manufacturers

## Slide 10: IA-32 Modes of Operation - 4
Virtual-8086 sub-mode
  hybrid of Protected Mode
  allow several sessions of Real-Address Mode
  each session is a MS-DOS virtual machine
  each program has its own 8086 computer
  if a MS-DOS virtual machine crashes, it does not affect the other process
  every virtual machine uses 1 MB of the central memory

## Slide 11: Referencias
Chapters: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de Ramón Ríos.
27-Ago-2019