## Slide 1: ORGANIZACIÓN Y PROGRAMACIÓN DE COMPUTADORAS
OPC
A – D 2019

## Slide 2: Direct vs Indirect Addressing - 1
With DIRECT addressing operands
  The operand has the content (value) of interest
    E.g.: mov EAX, alfa+4 ( or [alfa+4] )
With INDIRECT addressing operands
  The operand has the address (offset) of the content (value) of interest.
  The operand has a pointer (or a reference).
    E.g., pseudo-code: mov ESI, OFFSET alfa+4
    mov EAX, indirectESI
    After ESI=ESI+4, mov EAX, indirectESI ?

## Slide 3: Indirect Addressing Operands- 2
Two approaches
With Indirect operands
  [reg]
    reg contains an address (offset, pointer, or reference)
With Indexed operands (also, Indexed Addressing)
  constant [reg] [constant + reg]
    reg contains an index value or an address

## Slide 4: Indirect Addressing Operands - 3
reg: could be any general-purpose register
  Rmn, . . ., EAX, EBX, ECX, EDX ( 64, 32, 16, 8 and 8 bits )
  Rxy, . . ., ESI, EDI, EBP, ESP (64, 32 and 16 bits)
ESI and EDI prefered registers
  RSI, ESI: Source Index
  RDI, EDI: Destination Index
For each approach?
  How come, you get the effective address? ____
  How long (bits) must be the effective address and how much room do you need from the reg? ____

## Slide 5: Indirect Operands vIa
An indirect operand holds the address of a variable (pointer, offset, or reference), usually an ARRAY or STRING.
It can be dereferenced (just like a pointer).
In Protected Mode, any indirect operand can be any of the 32-bit or 64-bit general-purpose registers, surrounded by brackets.
Also, a memory place (DWORD / QWORD) can hold an address value.
General Protection Fault: in Protected Mode, if the effective address, points to an area outside your program’s data segment, the CPU executes a General Protection Fault (GP).

## Slide 6: Indirect Operands - 3a
.DATA
val1 BYTE 10h,20h,30h
.CODE
MOV ESI,OFFSET val1
MOV AL,[ESI] ; ESI=0000 0000h; AL = 10h
; Size of the content?___
INC ESI
MOV AL,[ESI] ; ESI=0000 ____h; AL = 20h
INC ESI
MOV AL,[ESI] ; ESI=0000 ____h; AL = 30h
An indirect operand holds the address of a variable, usually an array or string. It can be dereferenced (just like a pointer).

## Slide 7: Indirect Operands - 3b
.DATA
myCount WORD 0
.CODE
MOV ESI,OFFSET myCount
INC [ESI] ; error: ambiguous
INC WORD PTR [ESI] ; ok
Use PTR to clarify the size attribute of a memory operand.
Should PTR be used here?
ADD [ESI],20
yes, because [ESI] could point to a byte, word, or doubleword

## Slide 8: Pointers - 3c
.DATA
arrayW WORD 1000h,2000h,3000h
ptrW DWORD arrayW
.CODE
MOV ESI, ptrW
MOV AX,[ESI] ; AX = 1000h
You can declare a pointer variable that contains the offset of another variable (it must be 32-bit or 64-bit long).
Alternate format:
ptrW DWORD OFFSET arrayW

## Slide 9: Array Sum Example - 3d
.DATA
arrayW WORD 1000h,2000h,3000h
.CODE
  MOV ESI,OFFSET arrayW
  MOV AX,[ESI]
  ADD ESI,2 ;or better: ADD ESI,TYPE arrayW
  ADD AX,[ESI]
  ADD ESI,2
  ADD AX,[ESI] ; AX = sum of the array
Indirect operands are ideal for traversing an array. Note that the register in brackets must be incremented by a value that matches the array type.

## Slide 10: Direct and Indirect operands
Direct operands in two-operand instructions (f.i. CMP)
  CMP reg, reg
  CMP reg, mem
  CMP reg, imm
  CMP mem, reg
  CMP mem, imm
Direct operands in two-operand instructions (f.i. CMP)
  CMP reg, [reg] like direct operand CMP reg, ___
  CMP [reg], reg like direct operand CMP ___, reg
  CMP [reg], imm like direct operand CMP ___, imm

## Slide 11: Referencias
Capítulos: Irvine, Kip R. Assembly Language for x86 Processors.
Notas de referencia, Ramón Ríos
17-oct-2019