## Slide 1: OPC - Basic Concepts: Overview
Computer Structure - hardware
Assembly Language
Data Representation

## Slide 2: General Computer Structure
*PC
CPU
Buffers
I/O Module Controllers
Central
Memory
Instruction
Instruction
Instruction
Data
Data
Data
Data
.
.
.
.
.
IR
MAR
MBR
I/O AR
I/O BR
execution
unit
.
.
.
.
.
.
MAR - Memory Address Register
MBR - Memory Buffer Register
I/O AR - I/O Address Register
I/O BE - I/O Buffer Register
PC - Program Counter
IR - Instruction Register
SP – Stack Pointer
*Must be saved and restored
0
N
1
*SP
*PSW
BUS
Stored-program

## Slide 3: Assembly Language (AL)
What is an assembler?
What background should I have?
How does assembly language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?

## Slide 4: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
mov EAX, A
mul B
add EAX, C
call WriteInt
mov F, EAX
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000
- - - -

## Slide 5: Assembly Data Representation
Binary Numbers
Binary Addition
Integers
Storage Sizes
Unsigned Integers
Hexadecimal Integers

## Slide 6: Binary Numbers
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 7: Unsigned Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 8: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Bn-1  2n-1) + (Bn-2  2n-2) + ... + (B1  21) + (B0  20)
B = binary digit
binary 00001001 = decimal 9:
(12  23) + (12  20) = 910

## Slide 9: Translating Unsigned Decimal to Binary
37 = 100101
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
3710 = 1001012
B0
B1
B2
B3
B4
B5

## Slide 10: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 11: Integers and Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 12: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 13: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 0001011010100111100101002 to hexadecimal:

## Slide 14: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 15: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
  dec = (H3  163) + (H2  162) + (H1  161) + (H0  160)
Hex 123416 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,66010.
Hex 3BA416 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,26810.

## Slide 16: Converting Decimal to Hexadecimal
decimal 42210 = 1A616 hexadecimal
H0
H1
H2

## Slide 17: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, rem 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 18: Binary Subtraction
Subtract A – B
0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1
Practice: Subtract 0101 from 1001.

## Slide 19: Central Memory
Conformed by RAM
Ordered collection of bytes (like a vector)
Memory address as index of a byte
Each byte of the memory has a memory address for access

## Slide 20: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:
C6 75
A2 47
24 ??
-1
16 + 5 = 21
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?

## Slide 21: Referencias
Chapters: Tanenbaum, A. S.; Operating Systems.
Chapters: Irvine, Kip R.; Assembly Language for x86 Processors.
Notas: Ramón Ríos.
15-Ago-2019